# UV2000/2200(UV-VIS) Spectrophotometer

Features :

- Specially designed for industry and labs

- Pre-set wavelength program (4 wavelengths), 
and one-touch key response

- Single-point curve calibration and multi-point curve 
calibration (up to 12 points)

- Display of fitting degree of curve fitting and concentration 
data with up to 50 sets of curve parameters storage

- Display of concentration data with up to 200 sets of data storage

- System clock management/ Dark current calibration/ wavelength calibration/USB data communication

- Data-processing software

| Model | UV2000 | UV-2200 |
| --- | --- | --- |
| Optical System | Single beam, C-T type, 1200 lines/mm grating |
| Detector | Silicon photo diode |
| Light Source | Tungsten lamp (socket type, 20W / 12V, 2000 hours) Deuterium lamp (1000 hours) |
| Display Mode | 4.3” color LCD, touch screen |
| Wavelength Accuracy | ±2.0 nm (Calibrate by system automatically ) | ±1.5nm (Calibrate by system automatically ) |
| Wavelength Range | 200 - 1100nm | 190 - 1100nm |
| Spectral Bandwidth | 4nm | 2nm |
| Wavelength Repeatability | 1.0nm | 0.8nm |
| Stray Light | ≤0.5%T (220Nal) | ≤0.3%T (220Nal) |
| Photometric Range | T：-1.0 ~ 200.0%T ，A：-0.5 ~ 3.000Abs，F：0 ~ 9999，C：0 ~ 9999 |
| Photometric Accuracy | ±0.5%T | ±0.3%T |
| Photometric Repeatability | 0.2%T |
| Stability | dark current < 0.2%T, bright current < 0.5%T ±0.002A/h |

1. Technical specifications and standard configuration

1.1 Technical specification

| Model | UV2000 | UV2200PC |
| --- | --- | --- |
| Monochromator | C-T monochromator, 1200 L/mm holographic grating |
| Sensor | silicon photocell |
| Display Screen | 4.3 inch color touch-screen display, LCD |
| Wavelength Calibration | automatic calibration after starting up |
| Wavelength Resolution | 0.1 nm |
| Light Source | deuterium lamp (1000h), tungsten lamp (2000h, 20W/12V) |
| Light Switching Point | can be set, 294 nm - 365 nm |
| Wavelength Range | 200-1000 nm | 190-1100 nm |
| Spectral Bandwidth | 4 nm | 2 nm |
| Wavelength Accuracy | ±2.0 nm | ±1.0 nm |
| Wavelength Repeatability | 1.0 nm | 0.5 nm |
| Measuring Range | 0 ~ 200%T, -0.301 ~ 3.000Abs, -9999 ~ 9999C, -9999 ~ 9999F |
| Transmittance Accuracy | ±0.5 %T | ±0.3 %T |
| Transmittance Repeatability | 0.2 %T | 0.2 %T |
| Stray Light | 0.5 %T(at 220nm and 360nm) | 0.15 %T(at 220nm and 360nm) |
| Baseline Flatness | / | ≤±0.004 Abs |
| Baseline Drift | ≤0.002 Abs / half hour (after warm-up at 500 nm) |
| Data Output | USB interface |
| UV-Solution Software | / | Windows® - based |
| Power |  | 220V10% 50Hz 90VA / 110V10% 60Hz 90VA |
| Sample Holder | 4 trench 50mm adjustable sample holder (10mm, 20mm, 30mm, 40mm, 50mm, position-adjustable) |
| Instrument Dimension | 470mm X 380mm X 225mm (L*W*H) |
| Package Dimension | 650mm X 539mm X 370mm (L*W*H) |
| Net Weight | 10.5 Kg | 10.5 Kg |
| Gross Weight | 14.5 Kg | 15.0 Kg |

1.2 Standard configuration   (”●” means have, “/” means do not have)

| Name | Quantity | UV2000 | UV2200PC |
| --- | --- | --- | --- |
| Main Machine | 1 | ● | ● |
| Power Line | 1 | ● | ● |
| Quartz Cuvette (10 mm optical path) | 2 | ● | ● |
| Glass Cuvette (10 mm optical path) | 4 | ● | ● |
| Fuse | 2 | ● | ● |
| Main Machine Instruction | 1 | ● | ● |
| UV-Solution Software | 1 | / | ● |
| Software Instruction | 1 | / | ● |
| USB Cable | 1 | / | ● |